## Slide 1: Multi-agent system for advanced information processing in medicine
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>

## Slide 2: Multi-agent system for advanced information processing in medicine
Part I – Image Processing: a decentralized view
Part II – Multi-agent design
Part III – A Cooperative Framework for Brain MRI Segmentation
Part IV – Ambient Intelligence: the case of monitoring
Part V – Normative Multi-Agent System
Part VI – Abductive Agents for Human Activity Monitoring
Part VII – Evaluative Experiments
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>

## Slide 3: Part II - Agent-centered design
1. Motivations and origins
2. Issues and definitions
3. The interaction principle
4. The situated agent paradigm
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>

## Slide 4: 1. Motivations and origins
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>
First definition
  MAS (Multi-Agent system) : a system in which artificial entities, called agents, operate collectively, in a decentralized way, toward a given task
  These entities may be implemented on a physical or logical support
Development in the 70th of the theory of mind
  Intelligence is relying on individual competences + ability to interact with a physical and social environment (eg perceive and communicate)
  Reasoning does not resume to applying an a priori fixed sequence of expert rules but rather imply a collection of concurrent, heterogeneous and dynamically evolving processes
  Two simultaneous and complementary trends : Minsky - The Society of Mind / Vygotsky - The Mind in Society ;

## Slide 5: 1. Motivations and origins
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>
Minsky - The Society of Mind
A useful metaphor to think of intelligence is to consider a large system of experts or agencies that can be assembled together in various configurations to get things done ;
Minsky said, « ...each brain contains hundreds of different types of machines, interconnected in specific ways which predestine that brain to become a large, diverse society of partially specialized agencies » ;
Cognition is a distributed phenomenon ;
[Minsky 85]

## Slide 6: 1. Motivations and origins
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>
The mind in society : the origins of individual psychological functions are social ;
Every high-level cognitive function appears twice: first as an inter-psychological process and only later as an intra-psychological process ;
The new functional system inside the child is brought into existence in the interaction of the child with others (typically adults) and with artifacts ;
As a consequence of the experience of interactions with others, the child eventually may become able to create the functional system in the absence of the others ;
[Vygotsky 78]

## Slide 7: 1. Motivations and origins
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>
The distributed cognition paradigm
Cognition is no more envisaged as a purely local and isolated information processing but rather considered as :
  Context-dependent ;
  Temporally distributed : past reasoning may influence current processings ;
  Involving cooperation and communication with the physical and social environment ;
  Dynamically evolving as the result of its processings and interactions ;
[Hutchin 95]

## Slide 8: 1. Motivations and origins
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>
Limitations of classical AI
Considering problems of increasing complexity :
  Problems that are physically and functionally distributed ;
  Problems that involve heterogeneous data and expertise ;
  Problems in which data, information and knowledge is uncertain, incomplete and dynamically evolving ;
  Problems that can not be tackled by global problem solving methods ;

## Slide 9: 1. Motivations and origins
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>
From [Miksch 96]
Physical distribution

## Slide 10: 1. Motivations and origins
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>
Physical distribution

## Slide 11: 1. Motivations and origins
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>
Functional distribution
Task example : patient monitoring
  Sensing, interpretation and summarization of patient data
  Detection, diagnosis, and correction of critical situations
  Construction, refinement and revision of short-term and long-term therapy plans
  Control and supervision of monitoring devices
  Explanation of observations, diagnoses, predictions, and therapies based on the underlying anatomy and physiology

## Slide 12: 1. Motivations and origins
Heteregoneus knowledge and expertise
Various type of knowledge
  Clinical Knowledge of common problems, symptoms and treatments ;
  Biological knowledge of anatomy, physiology and pathophysiology ;
  Knowledge of fundamental physical models and fault conditions ;
Various types of expertise
  Patient monitoring : a team work involving members with complementary tasks and skills,
  which is most often staffed with new or inexperienced physicians and nurses ;
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>

## Slide 13: 1. Motivations and origins
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>
Complexity requires a local view
Complex system behaviour
often emerge as the dynamic interaction
between :
  The system components
  The system as a whole with the environment
  The environment with the individual components
The resulting dynamics, at the system level, may influence the environment which in turn will influence the component dynamics
Even when a clean formulation is possible, analytical approaches often involves concurrent expansion of recursive functions
Comp.1
Comp.2
Comp.N
System
Environment

## Slide 14: 1. Motivations and origins
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>
Complexity increases in such a way that the expression or prevision of all possible cases becomes prohibitive
This suggests to design entities fitted with own laws, to augment their capacity of internal adaptation, and thus of autonomy and autoorganisation
An alternative to single monolithic system design is the divide and conquer principle where a phenomenon is viewed as composed of a set of related and interacting sub-phenomena
The whole phenomenon is then described by several (hererogeneous) models accounting for its component behaviours, together with several (heterogeneous) models accounting for their interactions
Instead of designing a single « heavy » all-purpose system, create « light », case-based, narrow-minded units that have clearly identified objectives and background information necessary to successfully achieve their objectives
[Courant 94]

## Slide 15: 1. Motivations and origins
Main advantages :
  A complex global model usually depends on several parameters that are difficult to identify and to measure ;
  Models with higher degree of approximation with respect to the real phenomenon may be derived, because the decomposition allows to develop sub-models for very specific contexts ;
  Alternative sub-models may be employed for describing the same phenomenon (competitive models) ;
  Since the sub-parts of the phenomenon may overlap, the actions that each unit undertake to regulate these sub-parts may conflict ; fusion and/or negotiation mechanisms are then required
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>

## Slide 16: 2. Issues and definitions
Multi-agent system : a set of entities (agents) interacting in the exploitation of a common environment, toward a common global goal, with no centralised control or supervising unit
Multi-Agent Systems are such that:
  Each agent has incomplete information (local view) or capabilities to solve a problem
  There is no global system control, nor any global view of the system given to any single agent
At least two description levels
  Individual or local (agent knowledge and behavior)
  Social or global (styles of interaction and cooperation toward the achievement of global tasks)
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>

## Slide 17: 2. Issues and definitions
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>
A multi-agent system may be :
  Open : the set of agents is not predefined, new agents may be created on demand ;
  Closed : the set of agents is fixed in advance ;
  Homogeneous : all agents obey the same model ;
  Heterogeneous : agents fitted with different models, operating at various levels of grain, may co-exit ;
  Hybrid : human and non-human agents may collaborate « anonymously » to perform the task at hand ;

## Slide 18: 2. Issues and definitions
Main agent properties, beyond adaptivity or context-awareness
Autonomy : be able to act without direct intervention of other entities towards the achievement of its specific goals, have control over its own actions and internal state (Jennings 1995) vs a social property, something that includes consideration of other agents, or of global system-level requirements or norms (Boella 2002)
Pro-activity: self-initiated and future-oriented action that aims to change and improve the situation or oneselff (Parker, Williams & Turner, 2006); the only way to maintain a consistent coupling between processing structures and environments that are evolving, subject to unpredictable changes and uncertainty and too complex to be perceived completely (Sen, 2000)
Situatedness: agents and environments in a situated MAS constitute complementary parts of a complex system that can mutually affect each other (Maes 1990), a dependency loop to take place between the micro and the macro level, between individuals and collectives
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>

## Slide 19: 2. Issues and definitions
Reactive agent: simple behavior based on sensori-motor low-level representations, low proactivity/adaptation
Biological metaphor
No internal representation, no explicit goal
Instinctive behavior (stimulus/answer)
Limited communication abilities (via environmental traces like pheromones, or signals)
Self or implicit organization
Numerous small/light agents (100)
Cognitive agent: able to reason over the world to achieve goals and develop complex interaction schemes based on high level knowledge and skills
Social metaphor
Explicit representation of their goal, knowledge of themselves and other agents
Rational behavior, based on reasoning and decisions
Developed communication skills
Explicit social organization,resource sharing, task allocation and cooperation modes
Few complex/heavy agents (10)
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>

## Slide 20: 2. Issues and definitions
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>

## Slide 21: 2. Issues and definitions
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>
Environnement
Perception
Action
behaviour-
based layer
local
planning layer
cooperative
planning layer
Knowledge Abstraction
Knowledge base
Control unit
social models
mental models
world models

## Slide 22: 2. Issues and definitions
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>
Agents as intentional systems
Rational agent: an entity able to perceive and act upon its enviroment to accomplish goals, based on its competences, knowledge and belief
Predominant approach: treat agents as intentional systems that may be understood by attributing to them mental states such as :
  The beliefs that agents have ;
  The desires or goals that agents want to occur or to achieve ;
  The intentions or plans of action, what he actually intend to do to satisfy its desires
Notes: <number>

## Slide 23: Agent behaviour
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>
Do forever
  Receive observation (percept) ;
  Update internal model (beliefs) ;
  Deliberate to form intentions ;
  Use intentions to plan actions (means-end reasoning) ;
  Execute plan ;
Two essential points :
  The agents have bounded resources (including time) ;
  The world changes while deliberating, planning and executing and this can result in intentions and plans being invalidated ;

## Slide 24: 3. The interaction principle
Various forms: Communication, Task allocation, Cooperation, Coordination of actions, Resolution of conflict
Various situations: compatible/incompatible goals, sufficient/unsufficient resources or competences, indifference, cooperation or antogonism
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>
Goal | Resources | Comp. | Situation
Comp. | Suff. | Suff. | Full independence
Comp. | Suff. | Insuff. | Basic collab.
Comp. | Insuff. | Suff. | Congestion
Comp. | Insuff. | Insuff. | Coord. collab.
Incomp. | Suff. | Suff. | Ind. competition
Incomp. | Suff. | Insuff. | Coll. competition
Incomp. | Insuff. | Suff. | Ind. Res access Confl.
Incomp. | Insuff. | Insuff. | Full conflict

## Slide 25: 3. The interaction principle
Explicit communication
  Information sharing: the agents read and write information on a shared memory structure (the blackboard)
  Message passing: the agents exchange messages using a given communication protocol (point-to-point or broadcast)
Implicit communication
  The agents leave traces or signals in the environment, acknowledging their presence or action at a given location
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>
Agent
Agent
Agent
Agent
Message
KS
Blackboard
KS
KS
Infor-
mation

## Slide 26: 3. The interaction principle
Task allocation: objectives
  Decompose the problem into sub-problems ;
  Allocate the tasks to agents, according to their competences and specialities ;
  Re-organize during execution if necessary ;
Task allocation: approach
  Static : the allocation is performed a priori by the system designer ;
  Dynamic : the allocation is performed by the agents themselves (eg contract net) ;
  Hybrid : the initial allocation my be revised to account for changes in the environment (case of an open architecture in particular) ;
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>

## Slide 27: 3. The interaction principle
The Contract Net: given a task to perform, allocate it to the « best » agent, knowing the task characteristics, its eventual realization constraints, and considering the agent potential and effective capabilities to succeed ;
3 main steps :
  Sending of a call for a task / reception of the proposals by the contacted agents ;
  Selection of the best proposals / establishment of the contract(s) / reception of the result(s) ;
  Selection / construction of final result ;
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>

## Slide 28: 3. The interaction principle
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>
Sending a call for a task
Receiving the proposals
Selecting (some) proposer(s)
Receiving the answers
Constructing the final result

I can
0.95
I can
0.85
I can
0.45
Who can?
I realize
0.75
I realize
0.55

There it is

You realize
Give me

## Slide 29: 3. The interaction principle
Three cooperation styles may be distinguished [Hoc 96]
Confrontational cooperation : a task is performed by agents with competing competencies or viewpoints, operating on the same data set ; the result is obtained by fusion ; the emphasis is on competence distribution
Augmentative cooperation : a task is performed by agents with similar compe-tencies or viewpoints, operating concur-rently on disjoint subsets of data ; the result is obtained as a collection of partial results ; the emphasis is on data distribution
Integrative cooperation : a task is decomposed into sub-tasks performed by agents operating in a coordinated way with complementary competences, ; the result is obtained upon execution completion the emphasis is on goal distribution
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>

## Slide 30: 3. The interaction principle
How to plan and coordinate the actions of several agents in order to reach a common goal?
Two main modes : Planning (centralized or distributed) / Opportunistic
Centralized planning: a centralized manager distributes the plans to every agent, having the knowledge of their competences + competencies in task decomposition ; Easiest way to maintain consistency of problem solving but not too far from classical planning ;
Distributed planning: Each agent produces partial plans and communicate them to the other agents or to a mediator ; Issues : fuse/synchronize the plans in a consistent way ; avoid duplication of efforts + conflicts ; dynamic planning? Heavy communication load, high complexity
Opportunistic problem solving: the system chooses at each step the action that will allow the best progress toward the solution, given the curent situation (ie the available data and the intermediate state of problem solvng) ; Strongly data-directed, allow rapid refocusing (at each control cycle) ; Implies some knowledge of action cost and utility ;
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>

## Slide 31: 3. The interaction principle
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>
Resolution of conflicts, several solutions : Authoritary : a supervising agent has the authority and knowledge to take a decision ; Mediation : a mediator agent knows the various viewpoints and tries to solve the conflict ; Negotiation : the conflicting agents try to find a solution through several negotiation steps ;
Main negotiation steps :
  1. A makes a proposal ;
  2. B evaluates this proposal, determines the resulting satisfaction according to his own goals ;
  3. if B is satisfied, then STOP
  otherwise B elaborates a counter-proposal based on his own goals and constraints ;
  4. Go to step 2 with A and B roles exchanged ;

## Slide 32: 4. The situated agent paradigm
The agents are situated physically (at a given spatial or temporal location), semantically (for a given goal or task) and functionnally (with given models or competences) ;
These agents work in a specialized and local way, they produce partial results that are shared via the environment ;
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>
Model Space
Goal Space
Information Space
Agents
Knowledge Space

## Slide 33: 4. The situated agent paradigm
A dual adaptation:
  Internal adaptation by the selection of adequate processing models, according to the situations to be faced and to the goals to be reached ;
  External adaptation by the dynamical generation of constraints, eg of new sets of data and goals to explore ; such adaptation may requires the creation of new agents, modifying as a consequence the structure of the analyzing system itself ;
S. Giroux : Agents et systèmes, une nécessaire unité, PhD Thesis, 1993.
As the system works, it :
  completes its exploration, accumulates information, adapts and organizes according to the encoutered situations
  A constructive approach according to which the system, its environment and goals co-evolve
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>