## Slide 1: Multi-agent system for advanced information processing in medicine
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>

## Slide 2: Multi-agent system for advanced information processing in medicine
Part I – Image Processing: a decentralized view
Part II – Multi-agent design
Part III – A Cooperative Framework for Brain MRI Segmentation
Part IV – Ambient Intelligence: the case of monitoring
Part V – Normative Multi-Agent System
Part VI – Abductive Agents for Human Activity Monitoring
Part VII – Evaluative Experiments
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>

## Slide 3: Part III – A Cooperative Framework for Brain MRI Segmentation
I. Magnetic resonance imaging (MRI) in brief
II. A distributed, cooperative approach
III. Distributed Local MRF Models for Tissue and Structure Brain Segmentation
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>

## Slide 4: I. Magnetic resonance imaging (MRI) in brief
Brain MR image interpretation
Tissue segmentation (WM, GM, CSF) : intensity level distribution
Noise, partial volume effect, …
Anatomical structure segmentation (caudate nuclei, ventricules, sulci…)
Anatomical knowledge (shape, topology, location…)
Intra/inter-individual variability
Size of data (3D, 2563 voxels)
26-31 August 2013
<number>
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
Notes: <number>

## Slide 5: II. A distributed, cooperative approach
Automatic detection of cerebral tissues
Automatic delineation of the contour of the brain
Integration of heterogeneous segmentation methods
Integration of complementary cooperation styles
Situated specialized agents
L. Germond, M. Dojat, C.J. Taylor, C. Garbay, A cooperative approach for segmentation of MRI brain scans, Artificial Intelligence in Medicine, 20(1): 77-93 (2000)
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>
Skull
Cerebro-spinal fluid
Grey matter
White matter

## Slide 6: II. A distributed, cooperative approach
Knowledge model (Lundervold 95)
Topology-criterion
  White matter is surrounded by gray matter (GM), itself surrounded by cerebro-spinal fluid (CSF)
  GM can be modeled as a ribbon of approximately 2 mm width. Thus, if a pixel is less than δpixels far from the cortex boundary, it belongs to either GM or CSF.
Segmentation principle:
  Cortex contour-based detection
  Grey matter region-based detection
  White matter region-based detection
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>

## Slide 7: II. A distributed, cooperative approach
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>

## Slide 8: II. A distributed, cooperative approach
Deformable
Model
Segmentation Agents
Grey
Matter
White
Matter
Fusion
Retroaction ?
Yes, on same slice
Yes, on following slice
End
Contour Detection
No
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>

## Slide 9: II. A distributed, cooperative approach
Deformable model
A priori knowledge: set of 20 examples, aligned on a common AC-PC plane
Building: manual positioning of landmarks, PCA analysis
Features: robustness, global model
Cootes TF, Hill A, Taylor CJ and Haslam J. The use of active shape models for locating structures in medical images, Im. Vis. Comput. 1995;12:335-365.
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>
Position initiale
Position finale
après déformation

## Slide 10: II. A distributed, cooperative approach
Deformable model
The result provided by the model allows the derivation of spatial and topological information about the localization and local characteristics of the brain tissues
This information is then used by the multi-agents system (integrative cooperation)
Note, however, that the cortical boundary is only roughly detected, a precise delineation of the brain sulci remaining required (integrative cooperation)
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>

## Slide 11: II. A distributed, cooperative approach
Two classes of agents : region agents specialized for GM or for WM segmentation and edge agents specialized for the brain boundary detection
The agents are autonomous and simple entities implemented as C++ objects, which communicate through a shared environment and are concurrently executed under control of a scheduler
Each agent is locally specialized (augmentative cooperation) and initialized at runtime
RegionAgent operate according to region growing; this implies the definition of the initial localization in the image (seed) and the behavior (parameterSpecialization) of pixel growing agents
EdgeAgent operate according to optimum detection, based on heterogeneous information; this implies the specification of the bounds of the edge segment, the parameters of the cost function (costFunction) and a fusion function (confrontational cooperation)
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>

## Slide 12: II. A distributed, cooperative approach
Region growing agent
Initial seed
Parameters: μ, σ
Agregation criteria:
 - 1.5  < I(p) <  + 1.5 
Contour Agent A*
fusion between global and local contour detection + region information
Local contour detection: B-spline interpolation of the signal + hysteresis thresholding to detect tiny structures
The edge agents search for the best path (cost function c) between two extremities p1 and p2 placed on the brain boundary as assessed by the deformable model
This guaranties the conservation of global topology
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>

## Slide 13: II. A distributed, cooperative approach
Grey matter agents
Seed positioning based on the knowlegde model
Specialization (parameters computation) based on the selection of a tissue sample and a statistical computation: gaussian mixture model (grey matter + CSF)
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>

## Slide 14: II. A distributed, cooperative approach
White matter agents
Seed positioning based on knowledge model + previous grey matter detection, within non segmented areas
Specialization (parameters computation) based on the selection of a tissue sample + mean and variance computation
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>

## Slide 15: II. A distributed, cooperative approach
Contour detection agent
Goal: refine initial brain delineation
Approach: fusion between global and local contour detection + region information
Principle: dynamical programing
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>

## Slide 16: II. A distributed, cooperative approach
Issues: coherence of the information sources
Take advantage of the coherence and complementarity that exists between the information sources
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>

## Slide 17: II. A distributed, cooperative approach
Fuzzy combination performed from the distance maps (Chamfer distance)
Cost function fi(p) for each pixel p
fi(p) = (βIInterface(p) + γIEdge(p)) /(β+γ)
With βand γ weights, to account for the difference in precision between the two information sources
IInterface(p) the distance to the GM/CSF interface based on region segmentation
IEdge(p) the distance to the edge provided by the edge detector
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>

## Slide 18: II. A distributed, cooperative approach
The edge detected by the edge agents can be used as a replacement of the initial boundary detected by the deformable model, refining the initial contour
This step uses confrontational cooperation: the initial model-based information is replaced by the newly computed one, judged more accurate.
The whole segmentation process may then be launched again
Retroaction on an adjacent slice in the image volume (2,5D processing)
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>

## Slide 19: III. Distributed Local MRF Models for Tissue and Structure Brain Segmentation
Niveaux de gris
MG
MB
Fréquence
Niveaux de gris
Fréquence
MG
MB
Niveaux de gris
Fréquence
B. Scherrer, M. Dojat, F. Forbes, C. Garbay, Agentification of Markov model-based segmentation: Application to magnetic resonance brain scans, Artificial Intelligence in Medicine 46(1): 81-95 (2009)
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>
Notes: <number>

## Slide 20: III. Distributed Local MRF Models for Tissue and Structure Brain Segmentation
Tissue segmentation: We distribute local situated cooperative agents which estimate local intensity models (augmentative cooperation)
Structure Segmentation: We distribute local situated cooperative agents which introduce knowledge based on Fuzzy Spatial Relations (augmentative cooperation)
Markovian segmentation framework for a robust to noise segmentation, without any bias field modelization
Tissue and Structure segmentation are linked and mutually improve (integrative cooperation)
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>
Notes: <number>

## Slide 21: III. Distributed Local MRF Models for Tissue and Structure Brain Segmentation
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>

## Slide 22: III. Distributed Local MRF Models for Tissue and Structure Brain Segmentation
Tissue agents (CSF, GM, WM) estimate local intensity models
Structure agents (Frontal Horn, Caudate Nucleus…) use fuzzy spatial knowledge and perform fuzzy structure segmentation
For each agent : a local MRF model (augmentative cooperation)
Cooperation mechanisms between agents:
  Confrontative
    Tissue Agents  Tissue Agents to build local but consistent models
    Structure Agents  Structure Agents: to build and update the spatial relation maps
  Integrative
    Tissue Agents  Structure Agents: Each structure is composed of a tissue: tissue agents provide tissue intensity models to structures
    Structure Agents  Tissue Agents : Feedback of structure segmentation on Tissue segmentation
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>

## Slide 23: III. Distributed Local MRF Models for Tissue and Structure Brain Segmentation
Importance of subvolumes size
Agents with 40x40x40 voxels
  Good representation of tissue classes to ensure a reliable model estimation.
  Not really local, so sensitive to inhomogeneities
Agents with 10x10x10 voxels
  More local, so more robust to inhomogeneities.
  But under-representation of tissue classes to ensure a reliable model estimation
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>
Notes: <number>

## Slide 24: III. Distributed Local MRF Models for Tissue and Structure Brain Segmentation
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>
  Tissue Agents (800 to 1500 local agents) working over subvolumes
  Local markovian segmentation with K=3 { LCR, MG, MB }
  Cooperating with neighbouring tissue agents, to preserve global consistency of local intensity models, and with structure agents, to benefit from dynamically computed anatomical information
Structure agents (9 agents) working over spatial structures
  Markovian segmentation with K=2 (structure/non structure)
  Cooperating with tissue agents to compute their intensity models, and with structure agents to build and update their own models

## Slide 25
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>

## Slide 26: III. Distributed Local MRF Models for Tissue and Structure Brain Segmentation
Observations : Labels :
Perform the image segmentation (tissues) : maximize over z the probability
Spatial dependencies between voxels, providing a labeling regularization and a robust to noise segmentation
A priori knowledge of the brain spatial organization
EM-Based algorithms
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>
Spatial regularization term
External field term
A posteriori probabilities of overlapping
structure agents
Data driven term, based on intensities gaussian model

## Slide 27: III. Distributed Local MRF Models for Tissue and Structure Brain Segmentation
Local and cooperative EM Algorithm
  Model Checking: compute a local mean model over neighbouring agents
  Model Correction : if necessary, compute corrected model from a linear combination of estimated and mean models
  Model Interpolation: Compute one intensity model per voxel with cubic-spline interpolation
Benefits
  Ensures smooth model variation between neighboring agents
  Handles nonuniformity of intensity inside each agent
  Local easy-to-segment subvolumes converge quickly,
  allowing the system to focus on other areas
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>
Notes: <number>

## Slide 28: III. Distributed Local MRF Models for Tissue and Structure Brain Segmentation
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>
Agent Initialization
Idle Mode
Information diffusion
Model Checking
Global
Tissue
Agent
Set of Local Tissue Agents
Update probabilities
Update Model Parameters
Model Checking
over neighbourhood
Model Correction
Model Interpolation
Stabilized ?

## Slide 29: III. Distributed Local MRF Models for Tissue and Structure Brain Segmentation
Definition of one localized Structure Agent per Structure
For each structure agent AlS, a local MRF model Ml
2 Class Segmentation : structure / background
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>
Notes: <number>

## Slide 30: III. Distributed Local MRF Models for Tissue and Structure Brain Segmentation
Describe the brain anatomy according to stable relations between structures [Bloch I., 1999]
Generic and stable spatial relations provided by a brain anatomist: « The left caudate nucleus is at less than 5mm from the left frontal horn », « The right thalamus is below the right frontal horn »,…
A fuzzy knowledge frame to cope with the heavy inter-individual variability of the brain
Expressed via 3D fuzzy maps representing relations of distance, orientation (between structures), and symetry of the brain anatomy, followed by a fusion step
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>
Computation of symetrical object
Distance relation
Erosion

## Slide 31: III. Distributed Local MRF Models for Tissue and Structure Brain Segmentation
Ex: The Caudate Nucleus
The Fuzzy Localization Map provides the agent territory (dynamic localization, with a simple thresholding) and is integrated in the MRF framework (Local 2-Class Markov Model Ml for each structure l)
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>
a Fuzzy Localization Map of the structure in the volume
FUSION
Distance Relation
Orientation Relation
External field term: Integration of a priori knowledge based on Fuzzy map
Probability of the structure tissue
Notes: <number>

## Slide 32: III. Distributed Local MRF Models for Tissue and Structure Brain Segmentation
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>
Global
Tissue
Agent
Global
Structure
Agent
Structure Level
Tissue Level
Structure Agents
Tissue Agents
MRF Model Ml
MRF Model Mc
Intensity Models
External Field
Intensity Models
External Field

## Slide 33: Adaptation to local image complexity
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
Iteration number per agent
SPM5
FAST
LOCUS-T
High inhomogeneity (surface antenna)
LOCUS-T
SPM5
FAST
Real 3T Image
<number>

## Slide 34: III. Distributed Local MRF Models for Tissue and Structure Brain Segmentation
Improvement of tissue segmentation
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>
Segmentation result without anatomical knowledge
Introduction of anatomical knowledge: improvement of tissue segmentation around putamen and thalamus.
Initial image