## Slide 1: Multi-agent system for advanced information processing in medicine
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>

## Slide 2: Multi-agent system for advanced information processing in medicine
Part I – Image Processing: a decentralized view
Part II – Multi-agent design
Part III – A Cooperative Framework for Brain MRI Segmentation
Part IV – Ambient Intelligence: the case of monitoring
Part V – Normative Multi-Agent System
Part VI – Abductive Agents for Human Activity Monitoring
Part VII – Evaluative Experiments
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>

## Slide 3: Part VII – Evaluative Experiments
1. Data gathered, experimental conditions
2. Overview of results
3. Evaluating the system adaptation potential
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>

## Slide 4: 1. Data Gathered
Real data acquired using a monitoring belt (Zephyr BioHarness) from which we retrieve Heart- and Breath-Rates, Accelerometers, Cutaneous temperature and angle of the torso.
Two sets of data totaling more than twelve hours of monitoring:
  Office consists in annotated Activities of Daily Life (ADL) situations
  Outdoors includes both cycling in town and hiking in the Alps
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>

## Slide 5
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>
1. Data Gathered

## Slide 6: 1. Data Gathered
The data are noisy, and may contain freak values, for example when the person re-adjusts the monitoring belt, as it may chafe (especially with sweat during physical effort, or after a meal), or when removing a garment, etc.
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>

## Slide 7: 1. Data Gathered
« Collective dimension »: fusing data from several persons
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>

## Slide 8: 1. Data Gathered
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>
« Backpack Break » during a mountain Hiking session. Complementarity of Physiology and Actimetry: The Movement (Mvt, box A) and Position (Pos, longitudinal angle: box B) provide clues to an event (break) that is invisible with regards to Heart Rate (HR, bpm).

## Slide 9: 1. Data Gathered
The A box shows how the Heart Rate increases during a period of walking (in the mountains)
The B box shows that when the person stops, there is a delay before HR begins to decrease (recovery state). This delay supports our division of L2 States into Physiology and Activity categories, as knowledge about the physical activity allows us to anticipate on the physiology.
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>

## Slide 10: 2. Overview of results
A graphical interface provides a representation of the hypotheses likelihood over time.
The colored line represents the Ground Truth Micro-scenario (prex M): green if it appears likely, blue if unlikely. The dot colors represent the High, Medium, Low confidence ranges (resp. green, yellow, red). Each dot is 1 second. Arrows show agent creations.
The figure shows two predictive actions from the Basal Physiology State:
  Exploring new Micro-Scenarios (zoom E), which in turn create States for their own verification
  Anticipation, which is a result of a lower confidence value for at least anticipation.
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>

## Slide 11: 2. Overview of results
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>

## Slide 12: 3. Evaluating the system adaptation potential
Not aimed at checking the system accuracy, in terms of its mere results, but rather oriented toward the estimation of the interpretative process unfolding
Experimentation articulated around a set of functional and non-functional properties, some of which are supported by qualitative, analytical discussions, others by carefully defined quantitative measures
Functional claims:
  effectiveness: precision and recall
  efficiency (computing cost)
  sensitivity: adaptation to varying contextual frames
  robustness: ability to maintain a stable behavior, to recover from critical situations
Non-Functional claims:
  expressiveness: a wide variety of situations can be modeled and rules are declarative and open
  informativeness (extent of the hypothesis population at given times)
  utility: the system balances openness (exploration of new hypothetical frames) and focus (readability of the hypothesis population)
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>

## Slide 13: 3. Evaluating the system adaptation potential
Precision metrics Q function of the number of likely Micro-scenarios, nlikely(t)
  Q(t) = 0 if nlikely(t) = 0 ; Q(t) = 1/nlikely(t) otherwise
  The closer to 1 Q(t) is, the less ambiguity is obtained
Accuracy metrics Acc (RelAcc) function of the time spent in « relevant » hypotheses according to ground truth
  Acc = Ntrue/Ntotal with Ntrue the time spent with highly confident relevant hypotheses (« ground truth" Micro-Scenario considered likely); dependent on model quality
  RelAcc = Nactive/Ntotal with Nactive the time spent in examining relevant hypotheses (« ground truth » Micro-Scenario evaluated (regardless of how likely it then appeared). Relative Accuracy reflects how well the system chose its hypotheses
Time to Recovery
  TR: number of seconds a Probe stays in an Alarming policy after forcing policy revision. This measures how quickly the system reacts to interpretation failures.
Anticipation Success
  Rate ASR = x/nA where x is incremented each time a State agent receives a notification that one of its successors was validated. nA is the total number of times any State agent entered Anticipation. This measures the utility of prediction.
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>

## Slide 14: 3. Evaluating the system adaptation potential
Improving informativity by reducing ambiguity
Overall effect of forced anticipation (on the whole 2-hour Scenario): the number of agent is regulated, with less ambiguity in hypothesis management
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>

## Slide 15: 3. Evaluating the system adaptation potential
Disabled Probe version: a higher ASR, which is expected since the probe forces Anticipation in the State agents and therefore increases the number of unsuccessful anticipations, but a gain in Q (lss ambiguity)
26-31 August 2013
IEEE EMBS Summer School on Emerging Technologies and Applications in Telemedicine
<number>